5A10A Solar Controller                                                    domestic. For example, LED lighting, compact lighting systems, emergency lighting,

User instruction manual                                                   garden  lighting, stair lighting, camouflage lights, street lighting, wireless

Print version V3.1                                                      communication, security alarm, border police, traffic warning lights, traffic lights,

traffic yellow flashing lights, obstruction lights and so on.

Characteritics

1. Equipped with the MCU, artificially controlled.

2. Equipped with device to avoid the overcharge, over release, electronic short

circuit, over loading, battery inversely connecting, solar battery inversely

connecting.

3. Use the battery discharge rate characteristics to correct discharge control。

4.The series connection PWM circuit is implemented to form the major charging circuit,

make the voltage loss half of or lower than the diode charging circuit, and the

charging efficiency 3%-6% higher than the non-PWM.

Warnings for usage                                                             5. The LED shows the batteries current situation to make the customer get the

1、The batteries has stored much energy,please keep the batteries from the      information of the batteries.

short circuit under any circumstances,we strongly recommend connecting the      6. Three operating modes can be selected: normally open mode, the pure light

batteries with the fuse.                                                        control mode and light control plus timing mode.

2、Please avoid the short circuit wire and the terminal,for the wire and the    The drawings of the controlling panel              Cording diagram

terminal may generate voltage two times higher than the rated voltage of the

controller.Please use the insulated tools while operating the controller.

3、Ensure the children keep away from the battery and the controller.

4、Please comply with the manufacturer`s safety advice.

5、Because of the equipment work may have a fever, please keep ventilation.

6、The device pay attention to water，moisture，in order to avoid damage to

the equipment.

Suitable range

The controller is only applicable to solar power, rated voltage of11.1V

systems, battery of lithium battery cells..

Note: specifically how much battery charge, see the product model, product

can not be adapted to the various systems.                                         Outline dimension

Application	and Installation dimension

Widely used in power generation unmanned, remote mountain villages, wild and

Install and Method of using:                                              Technology index

| Model | 5A / 10A |
| --- | --- |
| Charging mode | PWM mode |
| System voltage | 11.1V |
| Power range | 5A≤55.5W；10A≤111W |
| Overload, short circuit protection | 1.25 times the rated current delay 5 minutes off, Automatic recovery after 5 minutes; ≥1.5 times the rated current of short-circuit protection action |
| Controller protection | Overload\Reverse\over-discharge\Over-charge\short protection |
| No-load loss | ≤5mA |
| Charge loop drop | ≤0.2V |
| Discharge loop drop | ≤0.1V |
| Overpressure protection voltage | 13.5V |
| Overpressure recovery voltage | 13.0V |
| Cut-off voltage | 12.6V |
| Over-discharge protection voltage | 9.0V |
| Over-discharge recovery voltage | 11.1V |
| Charge return | 11.1V |
| Do not set the voltage night | 3.0V |
| Do not set the voltage day | 7.0V |
| Protection degree | IP30 |
| Working temperature | －40℃～55℃ |
| Size | 53.4mm*68.6mm*22mm |
| Weight | 0.04kg |

Firstly, determine  the controller output mode , the device factory default setting is normally open mode .if you need to set for the pure light control mode or light control plus timing mode, you need to open the enclosure through set DIP switch, changing the discharge mode.

When the key set "ON" is 1, the key set "OFF" is 0, normally open, pure light control, light control timer mode corresponding key states plus the following table:

| 1234 Key | Mode | 1234 Key | Mode | 1234 Key | Mode | 1234 Key | Mode |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000 | On | 0100 | 4H | 1000 | 8H | 1100 | 12H |
| 0001 | Light control 1H | 0101 | 5H | 1001 | 9H | 1101 | 13H |
| 0010 | Light control 2H | 0110 | 6H | 1010 | 10H | 1110 | 14H |
| 0011 | Light control 3H | 0111 | 7H | 1011 | 11H | 1111 | Purelightcontrol |

1、Connecting the battery first. If correctly connected, battery indicator will light.

2、Connecting the wire of the solar panel second. If the connection is correct, the

indicator light of “CHARGE” will be on or flash 10 seconds later after laying

outside under the sun. Otherwise, please check the connection. Making sure the solar

energy panel is laid outdoors under the sunshine.

3、Connecting the load at the end. If inversely connected, the led lamp may be damaged.

Please pay attention to the anode and the cathode to avoid the inverse connection.

LED lights display instruction

| LED | State | Function |
| --- | --- | --- |
| CHARGE | Red light off | Night condition or the battery not connected |
|  | Rde light on | State of charge |
| BATTERY | Rde light on / Blink slowly | Low battery protection |
|  | Red light blinking | Battery power remaining 25% |
|  | Red and green flashing | Battery power remaining 50% |
|  | Green light blinking | Battery power remaining 75% |
|  | Green light always on | Battery power remaining 100% |
|  | Red and green flashing at the same time | Battery over-power |
| LOAD | Green ligh off/ always on | output shutdown/ output normal |

# Text boxes

Distinguished guests:

Thank you for selecting our product, please read the manual carefully before the usage.